## Slide 1: Stigmergy for Multi-Robot Coverage: Demonstration Presentation
Michael Chadwick

## Slide 2: Project Aims
Code a program to demonstrate the effectiveness of the Dark Room
  Target System: e-Puck platform
  Develop the ‘StiCo’ algorithm for the platform
  Should interact with the glowing floor in some manner
Construct a Dark Room
  Small enough to fit on a table approximately one meter in diameter
  Quick to set up; Quick to dismantle
  Uses glow in the dark foil as flooring

## Slide 3: Platform: E-Puck
An open hardware platform
  Designed mainly for educational purposes
Multiple sensors
  IR for kinetic, Camera for visual
LEDs allow visual representation of information
Project focuses use of:
  Camera to detect light trail on the floor
  LEDs to generate the light trail

## Slide 4: Algorithm: StiCo
StiCo is designed to aid patrolling robots
  Localised messages for indirect communication
  Light trail suggests a recently visited area
Circular movement pattern
  When light is detected, swap direction

## Slide 5: Arena
Boundaries are flexible to the user
  Restricted only to the size of the table in use
  Rope is tied between sturdy sections to provide arena limits
Arena edges can secure flooring underneath them
  Glow in the dark foil for this project

## Slide 6: Code Outline
Configure Camera
Infinite Loop:
  Start Camera
  Turn on ‘South’ LEDs
  Find lightest point in the current image
  Move away from the light source

## Slide 7: Test Cases
Can the arena hold the robot?
Is the flooring secure enough?
Can the camera pick up the trails?
Robot-based tests:
  Single robot interacting with activated flooring
  Multiple robots interacting with each other’s trails

## Slide 8: Human Data / Participants
No Human data has been used within this project currently
No Human data will be used for the remainder of the project

## Slide 9: Thank you for your time
Any Questions?